Crawford DL6010S Swingdock

Product description:

Stationary dock leveller with swing lip with:

Integrated frame with wall anchors (T-frames)

Electro-hydraulic operation with two lifting cylinders

Hydraulic cylinder swinging out of swing lip in highest platform position

Automatic, free floating position

One-button control unit with mains switch, including interlocking of leveller/door

Hold-to-run button to position lip on the truck bed and to put the leveller back in parking position

Hydraulic emergency stop in any operating position

Automatic mechanical locking in neutral position

Lateral torsion flexibility

Side plates (toe guards) with warning signs both above and below dock level

Internal wiring, plug connection

Power supply by others

Control Unit Protection Class IP 54

The dock leveller meets standard demands of most loading operations and fully complies with rules and regulations of the European Standard EN 1398

Dimensions:

| Dimensions | Vertical working range |
| --- | --- |
|  | LL 400 | LL 500 |
| NL OL GL LH | A | B | A | B |
| 2000 | NL+330 NL+190 600 | 260 | 280 | - | - |
|  | NL+330 NL+190 700 | 290 | 330 | 180 | 360 |
| 2250 | NL+330 NL+190 600 | 290 | 275 | - | - |
|  | NL+330 NL+190 700 | 300 | 345 | 180 | 380 |
| 2500 | NL+330 NL+190 600 | 310 | 270 | - | - |
|  | NL+330 NL+190 700 | 390 | 340 | 270 | 360 |
| 2770 | NL+330 NL+190 600 | 335 | 270 | - | - |
|  | NL+330 NL+190 700 | 400 | 340 | 290 | 360 |
| 3000 | NL+330 NL+190 600 | 340 | 265 | - | - |
|  | NL+330 NL+190 700 | 400 | 335 | 280 | 290 |
| 3500 NL+330 NL+190 800 | 495 | 335 | 390 | 345 |
| 4000 NL+330 NL+190 900 | 540 | 335 | 430 | 345 |
| 4500 NL+330 NL+190 900 | 590 | 335 | 480 | 345 |

Nominal width (NW) 1750, 2000, 2200. Load bearing capacity: 60 kN

Surface:

Surface painted in standard colour RAL 5010, thickness 80 µm

Lip bearing:

Reinforced steel tear plate swing lip

400 mm swing lip with 5° bend

40 mm bevelled lip

Hydraulics:

Standard oil for temperature range -20° to +60° Celsius

Control unit:

Voltage 400V, cable harness length 7m

Display of error messages

Service interval display

Readout function / Memory function

Options:

Frame

T-200 Frame (standard frame with a height of 200mm)

W-Frame (welded to pre-cast frame)

F-Frame (flat bar frame welded to existing frame or for replacement)

B-Frame (box frame, for positioning dock leveller and subsequent setting in concrete)

P-Frame (pit frame with support from under (made by others), up to NL=3000mm)

Surface

Surface painted in RAL 9005 / RAL 6005 / RAL 3002, thickness 80µm

Surface painted with coat thickness 160µm

Surface hot-dipped galvanised

Hydraulics

Low temperature oil for temperature range -30° to +60° Celsius

Bio-oil (environmental protection)

Lip bearing

Swing lip 500mm (only for LH700 and larger)

Bevelled lip 100 mm

Straight swing lip

Tapered swing lip

Energy & Ergonomics

EPDM gap sealing

Slip protection and noise reduction coating

Multifunctional docking control for direct control of dock leveller, dock shelter and door with just one control unit

Operating dock leveller and door

Operating dock leveller dock shelter and door

Operating dock leveller and dock shelter

Control unit

Impulse auto button to put the leveller back in parking position

Parking position detection

Voltage 400V

Cable harness extension

External EMERGENCY STOP button