Crawford DL6020T teledock

Product description:

Stationary dock leveller with telescopic lip with:

Integrated frame with wall anchors (T-frames)

Electro-hydraulic operation with two lifting cylinders

One hydraulic cylinder for infinitely-adjustable extension of steel lip

Automatic, free floating position

Three-button switch with standard main switch, incl. contact to lock door / leveller

Hold-to-run button to lift platform

Hold-to-run button to position the lip on the truck bed

Impulse auto button to put leveller back in parking position

Hydraulic emergency stop in any operating position

Automatic mechanical locking in neutral position

Lateral torsion flexibility

Side plates (toe guards) with warning signs both above and below dock level

Internal wiring, plug connection

Power supply by others

Control Unit Protection Class IP54

The dock leveller meets standard demands of most loading operations and fully complies with rules and regulations of the European Standard EN 1398

Dimensions:

Dimensions	Vertical working range 60 kN

LE 500

LE 1000	LE 345

| NL | LH | A | B | A | B | A | B |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2000 | 600 | 310 | 310 | 380 | 370 | 270 | 280 |
|  | 700 | 340 | 400 | 420 | 470 | 370 | 360 |
| 2500 | 600 | 420 | 260 | 500 | 290 | 380 | 225 |
|  | 700 | 430 | 370 | 510 | 420 | 400 | 340 |
| 3000 | 600 | 370 | 230 | 430 | 250 | 350 | 210 |
|  | 800 | 450 | 400 | 520 | 440 | 420 | 360 |
| 3500 | 800 | 520 | 400 | 600 | 440 | 490 | 360 |
| 4000 | 900 | 590 | 400 | 660 | 440 | 560 | 380 |
| 4500 | 900 | 570 | 410 | 640 | 440 | 550 | 380 |

Nominal width (NW) 1750, 2000, 2200, 2250mm for all sizes.

Surface:

Surface painted in standard colour RAL 5010, thickness 80 µm

Lip bearing:

Reinforced steel tear plate swing lip

500 mm telescopic lip

40 mm bevelled lip

Hydraulics:

Standard oil for temperature range -20°C - +60°C

Control unit

Voltage 400V 3-phase, 230V 3-phase, cable harness length 7m

Display of error messages

Service interval display

About function / Memory function

Impulse auto button to put the leveller back in parking position

Options:

Surface

Surface painted in RAL 9005, RAL 6005, RAL 3002, thickness 80 µm

Surface painted with coat thickness 160 µm

Surface hot-dipped galvanised

Frame

W-Frame (welded to pre-cast frame)

F-Frame (flat bar frame welded to existing frame or for replacement)

B-Frame (box frame, for positioning dock leveller and subsequent setting in concrete)

P-Frame (pit frame with support from under (made by others), up to NL=3000mm)

Hydraulics

Low temperature oil for temperature range -30°C - +60°C

Bio-oil (environmental protection)

Bridge bearing

Steel lip with front sill of 100mm

Lip in aluminium

Lip with oblique section 100mm

Lip with retracting tongues in steel, 1 per side (140mm)

Lip 1000mm

Energy & Ergonomics

EPDM seal

Slip protection and noise reduction coating

Front cover curtain PVC (up to nominal length 3000mm)

Multifunctional docking control for direct control of dock leveller, dock shelter and door with just one control unit

Operating dock leveller and door

Operating dock leveller dock shelter and door

Operating dock leveller and dock shelter

Control unit

Request parking position

Voltage 400V 3-phase, 230V 3-phase

Cable harness extension

External EMERGENCY STOP button