Crawford DL6030C combidock

Product description:

Combidock extending bridge:

Special construction for efficient loading and offloading of all sizes of vehicle, from truck to small transporter

Integrated frame with wall anchors (T-frames)

Electro-hydraulic operation with two lifting cylinders

Lip extension in aluminium, in three sections, each with an extender cylinder

Control unit with selector for "Big Truck" and "City van" operation

"Big Truck" operation:

The lip is extended completely in one piece, total width 2000mm

"City van" operation:

Only the central lip section is extended, width of central section 1000mm

When positioned on the vehicle the bearing strength is reduced to approx. 100kg

Automatic, free floating position

Hydraulic emergency stop in any operating position

Automatic mechanical locking in neutral position

Lateral torsion flexibility

Side plates (toe guards) with warning signs both above and below dock level

Internal wiring, plug connection

Power supply by others

Control Unit Protection Class IP55

The dock leveller meets standard demands of most loading operations and fully complies with rules and regulations of the European Standard EN 1398

Dimensions:

Dimensions	Vertical Working range

| NL | LH | A | B - inside LH* | B - down to LP |
| --- | --- | --- | --- | --- |
| 3000 | 800 | 450 | 375 | 550 |
| 3500 | 900 | 560 | 360 | 650 |
| 4000 | 930 | 590 | 390 | 650 |

* When tail lift is in use Nominal width (NW) 2000mm.

Load capacity:

"Big Truck" operation 60kN

"City van" operation 20kN

Surface:

Surface painted in standard colour RAL 5010, thickness 80µm

Hydraulics:

Standard oil for temperature range -20°C - +60°C

Control unit:

Voltage 400V 3-phase, 230V 3-phase , cable harness length 18m

Impulse auto button to put the leveller back in parking position

Options:

Surface

Surface painted in,RAL 3002, RAL 6005 or RAL 9005 thickness 80µm

Surface painted with coat thickness 160µm

Surface hot-dipped galvanised 80µm

Frame

W-Frame (welded to pre-cast frame)

Hydraulics

Low temperature oil for temperature range -30°C - +60°C

Bio-oil (environmental protection)

Energy & Ergonomics

EPDM gap sealing

Slip protection and noise reduction coating

Multifunctional docking control for direct control of dock leveller, dock shelter and door with just one control unit

Operating dock leveller and door