Albany HS8110P high speed door

Product description:

•	The HS8110P is designed for increased longevity and comfort in medium-sized heavy- duty exterior operations.

•	Unique door drive technology – a gear driven system consisting of a pinion on the drive shaft that forces the lateral retaining straps up or down and contains no ballast in the door curtain or tension straps.

•	Unique side column technology provides excellent seal on all 4 sides thereby reducing heat loss.

•	The speed of opening is up to up to 2,4 m/s depending on size of door.

•	The speed of closing is 1,2 m/s.

•	The door design withstands overpressure or underpressure in specific areas.

•	Photocells in side columns.

•	Dimensions: Min: 1000 mm x 2000 mm, Max: 5500 mm x 5500 mm

•	Wind load resistance: (EN 12424) Class 2 (450 Pa (N/m²)), (EN 12424) Class 3 (700 Pa (N/m²)) for doors up to W 4000 mm x H 5500 mm

•	Water penetration (EN 12425) Class 2, (50 Pa (N/m²))

•	Air permeability (EN 12426) Class 1 (24 m³/m²/h at 50 Pa)

•	Thermal transmittance (EN 12428) 6,02 W/(m²K)

•	Temperature working range: -20 °C to +40 °C

•	Door curtain 900 g/m² colored PVC, material thickness: 0,8 mm

•	Flexible door curtain without ridged parts.

•	Flexible soft bottom edge including wireless edge activator.

•	Break-away and self-repair function.

•	The door curtain is available in 8 standard colors.

•	Various window options available, material PVC, material thickness 2.0 mm.

•	The motor with frequency converter guarantees smooth and reliable operation.

•	Soft start/stop significantly prolongs motor lifespan.

•	Operator 400V 3-phase 1,5 kW 3 x 16A

•	Operator protection: IP65

•	Control unit with display, impulse Up and Down buttons, an emergency stop mushroom button and a mechanical main switch.

•	Control unit protection: IP54

•	Lifetime expectations: 1.000.000 cycles

•	Optional color for drum cover, side column cover and motor cover.

Options:

Stainless steel

o	Construction in stainless steel AISI304

o	Side column cover, stainless steel AISI304

o	Motor cover, stainless steel AISI304

o	Drum cover, stainless steel AISI304

Window and vision panel options:

o	small window 640x580 mm PVC

o	vision panel 400mm PVC

o	vision panel 800mm PVC

o	large window 1200x2400mm PVC

o

Door curtain color

o	yellow RAL 1003

o	orange RAL 2004

o	red RAL 3000

o	blue RAL 5002

o	green RAL 6005

o	grey RAL 7035

o	black RAL 9005

o	white RAL 9010

o	Dynalumin

Insulated door curtain

o	Insulated door curtain with static insulation of 2.41 W/m²K

•	Max. 4500 x 4500

•	With drum cover headroom +650

•	No windows

Cover options

Side column cover:

o	Galvanized steel

o	Painted in 8 standard colors

o	Special paint finish Motor cover:

o	Galvanized steel

o	Painted in 8 standard colors

o	Special paint finish Drum cover:

o	Galvanized steel

o	Painted in 8 standard colors

o	Special paint finish

Drive and control options:

o	Acoustic signal 24VAC 80 dB at 1 meter ( horn when door is moving)

o	Extra safety photocell

o	UPS 1 Phase 230V

o	UPS 3 Phase 400V

o	Function Auto/Manual (includes switch on the control box)

o	Function Manual closing with opening/closing using a common manual command (e.g. one single pull rope opens and closes the door)

o	Function Manual closing with separate impulse (e.g. 2 buttons ??)

o	Function Two opening heights I/II with manual selection (switch included)

o	Function Two opening heights I/II with automatic selection ( 2 different opening impulses)

o	Function Interlocking / Airlock

o	Heating Control box

o

Access and automations

o	Photocell open door

o	Remote control

o	Push button box with 1 opening button (arrow up)

o	Push button with 1 EMERGENCY STOP button

o	Push button with 1 EMERGENCY STOP with key

o	Box with large black "mushroom" button for opening

o	Key operated box open/close

o	Push button stop

o	Push button box 1-button

o	Push buttons for opening and for closing

o	Magnetic loop

o	Radar incl. remote control

o	Radar holder galvanized steel – 950 mm

o	Radar holder painted steel – 950 mm

o	Radar holder stainless steel – 950 mm

o	Traffic lights

o	Warning light Red

o	Warning light Green

o	Standard function flashing light

o	Standard function flashing light with pre-warning before closing and opening

o	Pull rope switch complete 5 m cord

o	Pull switch bracket in galvanized steel – L 3000 mm

o	Pull switch bracket in painted steel – L 3000 mm

o	Pull switch bracket in stainless steel – L 3000 mm

o	Wireless and batteryless pull rope switch 5 m cord

o	Wireless and batteryless push button box

o	Chain hoist